## Slide 1: Cellular Cryptography
Honors Option for NSSA 245
Alex Beaver

## Slide 2: Topics
What drove mobile network design?
How does authentication/ authorization happen?
How does transport-layer security work?

## Slide 3: Constraints of a Mobile Network
Radio roaming
Access method and core are independent
Billing and QoS

## Slide 4
© OpenStreetMap Contributors
Structure

## Slide 5
© OpenStreetMap Contributors
Structure

## Slide 6
SIM Card (SIM)
User Endpoint (UE)
Mobility Management Engine (MME)
Home Subscriber Server (HSS)
Base Station/Radio (eNB/ng-eNB)
Packet Core
Structure

## Slide 7
Chip for Network Authentication
Inside of the User Endpoint
Cryptographic Operations, Data Storage
Data about the subscriber
TPM to store keys
Duplicate of data on HSS
SIM Card (SIM)

## Slide 8
SIM Card (SIM)
User Endpoint (UE)
Mobility Management Engine (MME)
Home Subscriber Server (HSS)
Packet Core
Base Station/Radio (eNB/ng-eNB)

## Slide 9
Device that a user interacts with
Phone, Laptop, Car, Vending Machine
Contains the SIM Card
Radios to connect to the network
User Endpoint (UE)

## Slide 10
SIM Card (SIM)
User Endpoint (UE)
Mobility Management Engine (MME)
Home Subscriber Server (HSS)
Base Station/Radio (eNB/ng-eNB)
Packet Core

## Slide 11
Per Region
Part of the EPC
Owned by Serving Network
Manages connection to the network
Mobility Management Engine (MME)

## Slide 12
SIM Card (SIM)
User Endpoint (UE)
Mobility Management Engine (MME)
Home Subscriber Server (HSS)
Packet Core
Base Station/Radio (eNB/ng-eNB)

## Slide 13
Part of Packet Core
Owned by home carrier
Stores data about customers and SIM cards
Manages authentication, QoS, Billing, etc.
Home Subscriber Server (HSS)

## Slide 14
SIM Card (SIM)
User Endpoint (UE)
Mobility Management Engine (MME)
Home Subscriber Server (HSS)
Base Station/Radio (eNB/ng-eNB)
Packet Core
AAA

## Slide 15
© OpenStreetMap Contributors
AAA

## Slide 16: Authentication vs Authorization
Authentication
Who is a SIM card assigned to?
Is this a legitimate device?
Is this device on a legitimate network?
Authorization
Is a user allowed to roam on this network?
Can a user access certain carrier resources?
What QoS should this device expect?
AAA

## Slide 17: Authentication and Authorization
Challenge/Response
SIM/UE initiates a connection to MME
MME forwards SIM data to HSS
HSS gives a random value to the SIM, and tells MME what to expect as output

## Slide 18: Keys
Root is stored on HSS and derived on SIM
Derive down
Limit scope
  Add parameter at each step, cannot reverse upwards
HSS is a relay

## Slide 19: Keys
K is stored on SIM
Cipher Key, Integrity Key on HSS
  Derivation is Carrier-Specific
KASME is per SN/SEQ, on MME
KeNB adds COUNT, at eNodeB

## Slide 20: Minimize Computation
B
B
B
A
A
A
2
2
2
2

## Slide 21: Minimize Computation
B
B
B
A
A
A
2
2
2
2
Change eNodeB
K
CK, IK
SEQ
KASME
KeNB

## Slide 22: Minimize Computation
B
B
B
A
A
A
2
2
2
2
Change MME
K
CK, IK
SEQ
KASME
KeNB

## Slide 23: Minimize Computation
B
B
B
A
A
A
2
2
2
2
Change SN
K
CK, IK
SEQ
KASME
KeNB

## Slide 24: Opportunities for Failure
Incorrect MAC
SEQ Synchronization Failure
Incorrect AV type
Invalid Authentication (XRES ≠ RES)
Retransmission of (RAND, AUTN)

## Slide 25: Evolution Over Time
2G (GSM/GPRS): Phone Authenticated by Network
3G (UMTS/CDMA2000): Mutual Authentication
4G (LTE): Serving-Network-Specific Keys
5G: Authenticate with Home Network

## Slide 26: Downgrade Attack
2G (GSM/GPRS): Phone Authenticated by Network
3G (UMTS/CDMA2000): Mutual Authentication
4G (LTE): Serving-Network-Specific Keys
5G: Authenticate with Home Network
Broadcast
2G at super strong signal

## Slide 27: Network Components

## Slide 28
SGW
PGW
Data
Control
Serving Network
Home Network
MME
HSS
Internet
Carrier or Private Services
Radio
Base Station

## Slide 29: Strata
Access Stratum
Layer 2
Between UE and Base Station
Non-Access Stratum
Layer 3
Between UE and MME

## Slide 30: AS
Radio Resource Control (RRC) Protocol for signaling
Some unencrypted comm before encrypted
Packet Data Convergence Protocol for RRC & User Data
KRRCint | COUNT | BEARER | Direction
128 | 32 | 5 | 1

## Slide 31: NAS
All communication is integrity checked
After establishing algorithm, all communication encrypted
Key derived from HSS
IMEI always secret
KRRCint | COUNT | BEARER | Direction
128 | 32 | 5 | 1

## Slide 32: Algorithm-Independent

## Slide 34: Graveyard

## Slide 35: Keys
©2010 3GPP™

## Slide 36
Attach Request
PLMN Identity
 MCC
 MNC
 Cell ID

## Slide 37
AUTH INFO REQ
IMSI
Serving Network
Establishes
A device is legitimate
The serving network is allowed
EPS AV

## Slide 38: AV Authentication Vector
Data that is used to authenticate
Contains
  IMSI
  Local Key (KASME)
  RAND
  SEQ (Sequence)

## Slide 39
©2009 3GPP™

## Slide 40
AUTH INFO Answer
Random Number (RAND)
Expected Response (XRES)
Authentication Vector (AUTN)
EPS AV

## Slide 41
AUTH Req
Random Number (RAND)
Authentication Vector (AUTN)

## Slide 42
AUTH Req
Random Number (RAND)
Authentication Vector (AUTN)
Verify AUTN
Compute RES
Compute CK and IK
Cipher Key and Integrity Key

## Slide 43
©2009 3GPP™

## Slide 44
RES
Compute KASME

## Slide 45
RES
Compare Expected RES (XRES) and RES

## Slide 46: Sequence (SQN)
Radios are unreliable
No SQN can be used twice
  Once AUTN has been verified, will not accept same SQN with different AUTN
Must allow for out-of-order
  Reject on time elapsed or large gap